## Slide 1: The 2336 Box
By Ricky Han and Jacky Li
ME100 Final Project

## Slide 2: What the box does...
The 2336 box is a smart delivery box that can receive and weigh your package. It informs you via phone calls that you have a package delivered. It also has anti-theft mechanism that protects your packages from being stolen.

## Slide 3: Video Demonstration

## Slide 4: Computation (Main Control)

## Slide 5: Sensors
Accelerometer (theft detection)
4 Strain Gauges (weight measurement)
Matrix Pad (for password input)

## Slide 6: Strain Gauge (class HX711)

## Slide 7: Accelerometer (class Accelerometer)
data for warning
Fast interrupts for parallel computation with main program

## Slide 8: Matrix Pad (class Smartbox)
Alternate voltage of R1-4 in a for loop
Checking for voltage in C1-4
Implementation of single key input and multiple key inputs.

## Slide 9: Actuators
LED (the simplest user interface)
  Shows box state (on/off)
  Indicates key press on Matrix Pad
Servo Motor (Lid opening / closing)

## Slide 10: Servo Motor (class Servo)
Servo comes with microkit: 1.3kg*cm Torque
Estimated torque required to lift: 4.1 kg*cm
The servo we bought: 25kg*cm torque

## Slide 11: Communication (class Communication)
Two feeds in Adafruit.io
  Accelerometer feed
  Weight sensor feed
IFTTT
  Two applets
    If accelerometer value exceeds threshold, trigger message system.
    Measure and report weight after delivery received by box.

## Slide 12: Questions?